Extraction of the basic MOSFET (CD4007) parameters

using the 4145   semiconductor parameter analyzer

1. Extraction of the specific current IS

Using the current-based model for the long  n-channel MOSFET, one can readily prove that:

(1)

Additionally, if the MOS transistor operates in saturation, (1) can be written as:

(2)

According to expression (2), the ratio gms(t/ID = 1 deep in weak inversion (if<<1) and equal to 0.5 for if=8 (IF = ID = 8IS).

1.1. Use the circuit in Fig. 1 to determine IS. Set VG = 3.0V and measure the normalization current from gms/ID. (Note: The circuit in Fig. 1 operates in saturation for if<80.)

Fig. 1- Extraction of IS  from gms/ID

1.2. Using the methodology described in reference 2, find IS and VT0 of the MOSFET. Plot ID vs. VG and gmg/ID vs. VG. Your measurements should range from at least if ( 0.01 to if ( 100. What is the thermal voltage associated with your measurements? What is the approximate value of n in weak inversion?

1.3 Apply the methods to a p-channel transistor

## Extraction of VP

If the drain current is set to 3IS, as shown in the circuit of Fig. 2, then VP = VS. For VS in the range –0.2V to approximately 2.5V, plot the curve VS(VP) versus VG. Determine the value of VT0. Also plot .

Fig. 2: Circuit for the extraction of VP and n.

3. Write a technical report. You are expected to comment on the results, compare results with theory and with parameters provided by the foundry.

References:

- A. I. A. Cunha, M. C. Schneider and C. Galup-Montoro, "An MOS Transistor Model for Analog Circuit Design", IEEE J. Solid-State Circuits, vol. 33, no. 10, pp. 1510-1519, October 1998.

- A. I. A. Cunha, M. C. Schneider, C. Galup-Montoro, C. D. C. Caetano, and M. B. Machado, "Unambiguous extraction of threshold voltage based on the transconductance-to-current ratio", Workshop on Compact Modeling, Anaheim, USA, Proceedings of Nanotech 2005, pp.139 - 141, May 2005.